## Slide 1
Basic relationships and distance measures between pixels
Slides Credit: Lecture Slides from Paresh Kambe

## Slide 2: Pixel Neighborhood
  The pixels surrounding a given pixel. Most neighborhoods used in image processing algorithms are small square arrays with an odd number of pixels.

## Slide 3: Neighbors of a Pixel
f(0,0) f(0,1) f(0,2) f(0,3) f(0,4) - - - - -
f(1,0) f(1,1) f(1,2) f(1,3) f(1,4) - - - - -
f(x,y) = f(2,0) f(2,1) f(2,2) f(2,3) f(2,4) - - - - -
f(3,0) f(3,1) f(3,2) f(3,3) f(3,4) - - - - -
I I I I I - - - - -
I I I I I - - - - -
Y
X

## Slide 4: Neighbors of a Pixel
A Pixel p at coordinates ( x, y) has 4 horizontal and vertical neighbors.
Their coordinates are given by:
(x+1, y) (x-1, y) (x, y+1) & (x, y-1)
f(2,1) f(0,1) f(1,2) f(1,0)
This set of pixels is called the 4-neighbors of p denoted by N4(p).
Each pixel is unit distance from ( x ,y).
f(0,0) f(0,1) f(0,2) f(0,3) f(0,4) - - - - -
f(1,0) f(1,1) f(1,2) f(1,3) f(1,4) - - - - -
f(x,y) = f(2,0) f(2,1) f(2,2) f(2,3) f(2,4) - - - - -
f(3,0) f(3,1) f(3,2) f(3,3) f(3,4) - - - - -
I I I I I - - - - -
I I I I I - - - - -

## Slide 5: Neighbors of a Pixel
A Pixel p at coordinates ( x, y) has 4 diagonal neighbors.
Their coordinates are given by:
(x+1, y+1) (x+1, y-1) (x-1, y+1) & (x-1, y-1)
f(2,2) f(2,0) f(0,2) f(0,0)
This set of pixels is called the diagonal-neighbors of p denoted by ND(p).
diagonal neighbors + 4-neighbors = 8-neighbors of p.
They are denoted by N8(p). So, N8(p) = N4(p) + ND(p)
f(0,0) f(0,1) f(0,2) f(0,3) f(0,4) - - - - -
f(1,0) f(1,1) f(1,2) f(1,3) f(1,4) - - - - -
f(x,y) = f(2,0) f(2,1) f(2,2) f(2,3) f(2,4) - - - - -
f(3,0) f(3,1) f(3,2) f(3,3) f(3,4) - - - - -
I I I I I - - - - -
I I I I I - - - - -

## Slide 6: Adjacency
Adjacency: Two pixels are adjacent if they are neighbors and their intensity level ‘V’ satisfies some specific criteria of similarity. (e.g., They have same intensity value )
In binary images, 2 pixels are adjacent if they are neighbors & have same intensity values.
In gray scale, image contains more gray level values in range 0 to 255, and in binary image they are in range 0 and 1.
i.e., Binary image = { 0, 1}
Gray scale image = { 0, 1, 2, ------, 255}

## Slide 7: Adjacency
4-adjacency: Two pixels p and q with the values from set ‘V’ are 4-adjacent if q is in the set of N4(p).
e.g. V = { 0, 1}
1 1 0
1 1 0
1 0 1
p in RED color
q can be any value in green color.

## Slide 8: Adjacency
8-adjacency: Two pixels p and q, with the values from set ‘V’, are 8-adjacent if q is in the set of N8(p).
e.g. V = { 1, 2}
0 1 1
0 2 0
0 0 1
p in RED color
q can be any value in green color

## Slide 9: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p) OR
q is in ND(p) & the set N4(p) n N4(q) have no pixels whose values are from ‘V’.
e.g. V = { 1 }
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 i

## Slide 10: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p)
e.g. V = { 1 }
(i) b & c
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I

## Slide 11: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p)
e.g. V = { 1 }
(i) b & c
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I
Soln: b & c are m-adjacent.

## Slide 12: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p)
e.g. V = { 1 }
(ii) b & e
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I

## Slide 13: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p)
e.g. V = { 1 }
(ii) b & e
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I
Soln: b & e are m-adjacent.

## Slide 14: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p) OR
e.g. V = { 1 }
(iii) e & i
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I

## Slide 15: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in ND(p) & the set N4(p) n N4(q) have no pixels whose values are from ‘V’.
e.g. V = { 1 }
(iii) e & i
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I

## Slide 16: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in ND(p) & the set N4(p) n N4(q) have no pixels whose values are from ‘V’.
e.g. V = { 1 }
(iii) e & i
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I
Soln: e & i are m-adjacent.

## Slide 17: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p) OR
q is in ND(p) & the set N4(p) n N4(q) have no pixels whose values are from ‘V’.
e.g. V = { 1 }
(iv) e & c
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I

## Slide 18: Adjacency
m-adjacency: Two pixels p and q with the values from set ‘V’ are m-adjacent if
q is in N4(p) OR
q is in ND(p) & the set N4(p) n N4(q) have no pixels whose values are from ‘V’.
e.g. V = { 1 }
(iv) e & c
0 a 1 b 1 c
0 d 1 e 0 f
0 g 0 h 1 I
Soln: e & c are NOT m-adjacent.

## Slide 19: Connectivity
Connectivity: 2 pixels are said to be connected if their exists a path between them.
Let ‘S’ represent subset of pixels in an image.
Two pixels p & q are said to be connected in ‘S’ if their exists a path between them consisting entirely of pixels in ‘S’.
For any pixel p in S, the set of pixels that are connected to it in S is called a connected component of S.

## Slide 20: Paths
Paths: A path from pixel p with coordinate ( x, y) to pixel q with coordinate ( s, t) is a sequence of distinct pixels with coordinates (x0, y0), (x1, y1), ….., (xn, yn) where
(x, y) = (x0, y0)
& (s, t) = (xn, yn)
Closed path: (x0, y0) = (xn, yn)

## Slide 21: Paths
Example # 1: Consider the image segment shown in figure. Compute length of the shortest-4, shortest-8 & shortest-m paths between pixels p & q where,
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 22: Paths
Example # 1:
Shortest-4 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 23: Paths
Example # 1:
Shortest-4 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 24: Paths
Example # 1:
Shortest-4 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 25: Paths
Example # 1:
Shortest-4 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 26: Paths
Example # 1:
Shortest-4 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 27: Paths
Example # 1:
Shortest-4 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3
So, Path does not exist.

## Slide 28: Paths
Example # 1:
Shortest-8 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 29: Paths
Example # 1:
Shortest-8 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 30: Paths
Example # 1:
Shortest-8 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 31: Paths
Example # 1:
Shortest-8 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 32: Paths
Example # 1:
Shortest-8 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 33: Paths
Example # 1:
Shortest-8 path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3
So, shortest-8 path = 4

## Slide 34: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 35: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 36: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 37: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 38: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 39: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3

## Slide 40: Paths
Example # 1:
Shortest-m path:
V = {1, 2}.
4 2 3 2 q
3 3 1 3
2 3 2 2
p 2 1 2 3
So, shortest-m path = 5

## Slide 41: Distance Measures
City Block Distance: The D4 distance between p & q is defined as
D4( p, q) = |x - s| + |y - t|
In this case, pixels having D4 distance from ( x, y) less than or equal to some value r form a diamond centered at ( x, y).
2
2 1 2
2 1 0 1 2
2 1 2
2
Pixels with D4 distance ≤ 2 form the above contours of constant distance.

## Slide 42: Distance Measures
Chess-Board Distance: The D8 distance between p & q is defined as
D8( p, q) = max( |x - s| , |y - t| )
In this case, pixels having D8 distance from ( x, y) less than or equal to some value r form a square centered at ( x, y).
2 2 2 2 2
2 1 1 1 2
2 1 0 1 2
2 1 1 1 2
2 2 2 2 2
Pixels with D8 distance ≤ 2 form the above contours of constant distance.