## Slide 1: COMPUTER ORGANIZATION AND ASSEMBLY LANGUAGE (COAL CSC321)

## Slide 2: INTRODUCTION TO IBM PC ASSEMBLY LANGUAGE

## Slide 3: Assembly Language Syntax
An assembly language is an extremely low-level programming language that has a 1-to-1 correspondence to machine code the series of binary instructions which move values in and out of registers in a CPU (or other microprocessor).
Assembly language programs are translated into machine language instructions by an assembler, so they must be written to conform to the assembler's specifications.
An assembly language program consists of statements.
    Statement 2. directive

## Slide 4: RULES
Only one statement is written per line
Each statement is either an instruction or an assembler directive
instruction is translated into machine code
assembler directive instructs the assembler to perform some specific task, such as allocating memory space for a variable or creating a procedure

## Slide 5: Program Statement
The general format for an assembly language program statement is as follows:
name operation operand’(s) comment
Examples:
An example of an instruction is,
START: MOV CX,5 ; initialize counter
An example of an assembler directive is,
MAIN PROC

## Slide 6: Name Field
This field is used for:
  instruction label: if present, a label must be followed by a colon (:)
  procedure names
  variable names.
  Note: The assembler translates names into memory addresses.

## Slide 7: Name Field Rules:
Assembler translates names into memory addresses.
Names can be from 1 to 31 characters long: (letters, digits, and special characters: ?, ., _, $, @, %)
Embedded blanks are not allowed, names may not begin with a digit,
A name should not begin with a digit
A name may begin with a letter or a special character
If a period (.) is used, it must be the first character
Names are not case sensitive
Assembly language imposes some rules on how names are assigned to labels, variables, procedures and macros. It is the assembler's function to translate those names into memory addresses.

## Slide 8: 4.1.1 Name Field
Examples:
Legal Names Illegal Names
COUNTER1 2ABC (contains a blank )
@CHARACTER TWO WORDS (begins with a digit)
$500 A45.26 (. not first character)
SUM_OF_DIGITS YOU&ME (contains an illegal character)
.TEST
DONE?

## Slide 9: 4.1.2 Operation Field
For an instruction
This field consists of a symbolic operation code, known as op-code
The opcode describes the operation’s function ( MOV, ADD, SUB. )
Symbolic op-codes are translated into machine language opcode.

## Slide 10: 4.1.2 Operation Field
For an assembler directive
This field consists of a pseudo-operation code (pseudo-op)
Pseudo-ops are not translated into machine code;
pseudo-ops tell assembler to do something i.e.(SUM, PROC, NEAR) For example, the PROC pseudo-op is used to create a procedure.

## Slide 11: 4.1.3 Operand Field
1. For an instruction,
This field specifies data to be acted on. It may have one, two or no operands at all.
  Examples of instructions with different operand fields
  NOP ; Instruction with no operand field
  INC AX ; Instruction with one operand field
  ADD AX, 2 ; Instruction with two operand field
If 2 operands: the first is destination [It is the register or memory location where the result is stored (note: some instructions don't store the result)]., the second is the source operand
2. For an assembler directive,
the operand field usually contains more information about the directive.

## Slide 12: instructions for the 8086 processor These instructions may be classified into different classes. The following table summarizes the different classes of instructions, together with examples of each class.

## Slide 13: 4.1.4 Comment Field
A semicolon marks the beginning of a comment
A semicolon in the beginning of a line makes it all a comment line
Good programming practice dictates the use of a comment on almost every line.
Do not say something that is obvious. Put instruction in context of program
Example,
MOV CX, 0 ; Move 0 to CX. (This is not a good comment.)
MOV CX, 0 ; CX counts terms, initially set to 0. (This is a good comment.)

## Slide 14: Program Data
The processor operates only on binary data.
Thus, the assembler must translate all data representation into binary numbers.
However, in an assembly language program we may express data as binary, decimal, or hex numbers, and even as characters.
Numbers
A binary number is written as a bit string followed by the letter “B“ or "b"; for example, 1010B
A decimal number is a string of decimal digits, ending with an optional "D" or "d".
A hex number must begin with a decimal digit and end with the letter "H" or "h"; for example, 0ABCH
NOTE:
  (the reason for this is that the assembler would be unable to tell whether a symbol such as "ABCH" represents the variable name "ABCH" or the hex number ABC).

## Slide 15: Numbers
Examples:
Use a radix symbol (suffix) to select binary, octal, decimal, or hexadecimal
number type
        1010 decimal
        1010B binary
        -2134D decimal
        ABFFH illegal
        0ABFFH hex
        1BHH illegal
        1BFFH hex
        1,23 illegal
Signed numbers represented using 2’s complement.

## Slide 16: Characters
Characters and character strings must be enclosed in single or double quotes; ‘A' , “hello“.
Assembler translates characters to their ASCII code
( so there is no difference between using “A” and 41H)

## Slide 17: Variables
Each variable has a type and assigned a memory address.
Data-defining pseudo-ops
  DB define byte
  DW define word
  DD define double word (two consecutive words)
  DQ define quad word (four consecutive words)
  DT define ten bytes (five consecutive words)
Each pseudo-op can be used to define one or more data items of given type.

## Slide 18: Byte variables

## Slide 19: Word variables ( 2 bytes)

## Slide 21: Array Examples
In assembly language, an array is just a sequence of memory bytes or words. for example, to define a three-byte array called B_ARRAY, whose initial values are 10h, 20h, and 30h, we can write,
B_ARRAY DB 10, 25, 20
If array starts at offset address 0200h, it will look like this:
    Symbol Address Contents
    B-ARRAY 0200H 10
    B-ARRAY+1 0200H+1 25
    B-ARRAY+2 0200H+2 20

## Slide 22: Arrays in Assembly Language
In assembly language, an array is just a sequence of memory bytes or words.
There are two ways to define an array in assembly language.
Initialized Lists
An initialized array is defined in the same way as a scalar variable, but with multiple initial values.
scores: .word 100, 78, 63, 88, 52, 91, 75
Uninitialized Memory Blocks
Uninitialized arrays are defined using the .space directive.
scores: .space 400
Caution
The .space directive allocates the specified number of bytes. Specifying the desired number of array elements is a common mistake.

## Slide 23: Array Examples
W_ARRAY DW 0FFFFh, 789Ah, 0BCDEh
If array starts at offset address 0100h, it will look like this:
(To access an array in assembly language, we use a pointer. A pointer is simply a register or variable that contains a memory address.
The value in the pointer is computed as shown in the previous sections by adding the base address of the array and the offset of the desired element)
        Symbol Address Contents
        W_ARRAY 0100H FFFFH
        W_ARRAY+2 0102H 789AH
        W_ARRAY+4 0104H BCDEH

## Slide 24: Character strings
Examples:
1)
LETTERS DB ‘AaBCbc‘
Is equivalent to
LETTERS DB 41H,61H,42H,43H,62H,63H
2)
MSG DB ‘ABC‘,0AH,0DH,‘$‘
Is equivalent to
MSG DB 41H,42H,43H,0AH,0DH,24H

## Slide 25: QUESTION Show how character string “RG 2z” is stored in memory starting at address 0
SOLUTION:-
Address | Character | ASCII Code (HEX) | ASCII Code (Binary) 18 [Memory Contents]
0 | R | 52 | 0101 0010
1 | G | 47 | 0100 0111
2 | Space | 20 | 0010 0000
3 | 2 | 32 | 0011 0010
4 | z | 7A | 0111 1010

## Slide 26: Constant Declaration
In an assembly language program, constants are defined through the use of the EQU (Equates) directive.
Syntax:
Name EQU constant
The EQU directive is used to assign a name to a constant.
Use of constant names makes an assembly language easier to understand.
No memory is allocated for a constant.
The symbol on the right of EQU cab also be a string

## Slide 27: Constant Declaration
Examples:
1)
LF EQU 0AH ; LF can be used in place of 0Ah
MOV DL LF
MOV DL 0AH
2)
PMT EQU ‘TYPE YOUR NAME‘ ;
instead of
MSG DB ‘TYPE YOUR NAME‘
We can use
MSG DB PMT
Have the same machine code

## Slide 28: BASIC INSTRUCTIONS
MOV and XCHG

## Slide 29: MOV instruction
Is used to transfer data :
  between registers,
  between a register & a memory location.
  Or
  To move a number directly into a register or memory location.

## Slide 30: Syntax
MOV destination , source
Example:
MOV AX , WORD1
This reads “ Move WORD1 to AX “
The contents of register AX are replaced by the contents of the memory location WORD1.

## Slide 31: Mov AX , WORD1
Before
After
AX
AX
WORD1
WORD1
0006
0008
0008
0008

## Slide 32: MOV AH , ‘A’
This is a move of the 041h ( the ASCII code of “A” ) into register AH.
The previous value of AH is overwritten ( replaced by new value )

## Slide 33: XCHG instruction
(Exchange) operation is used to exchange
  the contents of
  two registers, or
  a register and a memory location

## Slide 34: Syntax
XCHG destination , source

## Slide 35: Example
XCHG AH , BL
This instruction swaps the contents of AH and BL.

## Slide 36: XCHG AH , BL
Before
After
AH AL
1A
AH AL
BH BL
BH BL
00
05
00
00
05
00
1A

## Slide 37: Example
XCHG AX , WORD1
This swaps the contents of AX and memory location WORD1.

## Slide 38: Restrictions on MOV
Example :
ILLEGAL : MOV WORD1 , WORD2
LEGAL:
MOV AX , WORD2
MOV WORD1 , AX

## Slide 39: ADD & SUB
Are used to add & subtract the contents of
  two registers,
  a register & memory location , or
  a register and a number
  memory location and a number.

## Slide 40: Syntax
ADD destination , source
SUB destination , source

## Slide 41: Example
ADD WORD1 , AX
This instruction , “ Add AX to WORD1 “ , causes the contents of AX & memory word WORD1 to be added, and the sum is stored in WORD1. AX is unchanged.

## Slide 42: Example
SUB AX , DX
This instruction , “ Subtract DX from AX “ , the value of DX is subtracted from the value of AX , with the difference being stored in AX. DX is unchanged.

## Slide 43: Example
ADD BL , 5
This is an addition of the number 5 to the contents of register BL.

## Slide 44: ILLEGAL
ADD BYTE1 , BYTE2
Solution :
move BYTE2 to a register before adding
MOV AL , BYTE2 ; AL gets BYTE2
ADD BYTE1 , AL ; add it to BYTE1

## Slide 45: INC ( increment )
Is used to add 1 to the contents of a
    Register or
    Memory location

## Slide 46: DEC ( decrement )
Is used to subtract 1 from the contents of a
    Register or
    Memory location

## Slide 47: Syntax
INC destination
DEC destination

## Slide 48: Example
INC WORD1
adds 1 to the contents of WORD1

## Slide 49: Example
DEC BYTE1
subtracts 1 to the variable BYTE1

## Slide 50: NEG (negate)
Is used to negate the contents of the destination.
It does this by replacing the contents by its two’s complement.

## Slide 51: Syntax
NEG destination
The destination may be a
register or
memory location.

## Slide 52: NEG BX
0002
FFFE
Before
After
BX
BX

## Slide 53: Translation of HLL to Assembly Language
Statement Translation
B = A MOV AX , A ; moves A into AX
MOV B , AX ; and then into B
WHY
Because direct memory – memory move is illegal we must move the contents of A into a register before moving it to B.

## Slide 54: Translation of HLL to Assembly Language
Statement Translation
A = 5 – A MOV AX , 5 ; put 5 in AX
SUB AX , A ; AX…. 5 – A
MOV A , AX ; put it in A

## Slide 55: Translation of HLL to Assembly Language
Statement Translation
A = B – 2 * A MOV AX , B ; AX has B
SUB AX , A ; AX has B – A SUB AX , A ; AX has B – 2 * A
MOV A , AX ; move results to B

## Slide 56: Program Structure
Machine language programs consist of :
  Codes,
  Data, and
  Stack.
  Each part occupies a memory segment. They are structured as program segments. Each program segment is translated into a memory segment by the assembler.

## Slide 57: Memory Models
The size of the code & data a program can have is determined by specifying a memory model using the . MODEL directive.

## Slide 58: Syntax
. MODEL memory_mode1
SMALL
MEDUIM
COMPACT
LARGE
Code in one segment
Data in one segment
Code in more than one segment
Data in one segment
Code in one segment
Data in more than one segment
Code in more than one segment
Data in more than one segment
No array larger than 64K bytes.

## Slide 59
Unless there is a lot of code or data, the appropriate model is SMALL.
. MODEL directive should come before any segment definition.

## Slide 60: Data Segment
A program’s data segment contains all the variable definitions. Constant definitions are made here as well, but they may be placed elsewhere in the program since no memory allocation is involved.
We use the . DATA directive followed by variable & constant declarations.
Variable addresses are computed as offsets from the start of this segment

## Slide 61: Example
.DATA
WORD1 DW 2
WORD2 DW 5
MSG DB ‘ This is a message ‘
MASK EQU 10010010B

## Slide 62: Stack Segment
Used to set aside storage for the stack
Stack addresses are computed as offsets into this segment
Use: .stack followed by a value that indicates the size of the stack

## Slide 63: Declaration Syntax
.STACK size
An optional number that specifies the stack area size in bytes.

## Slide 64: Example
.STACK 100 H
Sets aside 100h bytes for the stack area ( a reasonable size for most applications ) .
If size is omitted , 1 KB is set aside for the stack area.

## Slide 65: Code Segment
It contains a program’s instructions.

## Slide 66: Syntax
.CODE name
Optional name for the segment
Why??
there is no need for a name in a SMALL program
The assembler will generate an error

## Slide 67: Inside the code segment
Instructions are organized as procedures.
The simplest procedure definition is :
name PROC
; body of the procedure
name ENDP
name is the name of the procedure, PROC and ENDP are pseudo-op that delineate the procedure

## Slide 68: Example
.CODE
MAIN PROC
; main procedure body
MAIN ENDP
; other procedures go here

## Slide 69: Program Structure
A program has always the following general structure:
.model small ;Select a memory model
.stack 100h ;Define the stack size
.data
; Variable and array declarations ; Declare variables at this level
.code
main proc
; Write the program main code at this level
main endp
;Other Procedures
; Always organize your program into procedures
end main ; To mark the end of the source file