## Slide 1: The Stack and Introduction to Procedures

## Slide 2: The Stack
The stack segment of a program is used for temporary storage of data and addresses
A stack is a one-dimensional data structure
Items are added to and removed from one end of the structure using a "Last In - First Out" technique (LIFO)
The top of the stack is the last addition to the stack
The statement .STACK 100H in your program sets aside a block of 256 bytes of memory to hold the stack
The SS (Stack Segment Register) contains the segment number of the stack segment

## Slide 3: The Stack (cont’d)
The complete segment:offset address to access the stack is SS:SP
Initially before any data or addresses have been placed on the stack, the SP contains the offset address of the memory location immediately following the stack segment

## Slide 4: Empty Stack
Offset
0000
0002
0004
0006
0100
0100
SP:
(Beyond the end of the stack)

## Slide 5: PUSH Instruction
PUSH instruction adds a new word to the stack
SYNTAX: PUSH source
  where source is a 16-bit register or memory word
PUSH instruction causes the stack pointer (SP) to be decreased by 2. Then a copy of the value in the source field is placed in the address specified by SS:SP.
Because each PUSH decreases the SP, the stack is filled a word at a time backwards from the last available word in the stack toward the beginning of the stack.

## Slide 6: How Words Are Added To Stack
If stack is empty, SP has a value of 100h; otherwise it has a value between 0000-00FEh
SP:
0100
(Beyond the end of the stack)
SP
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE

## Slide 7: How Words Are Added To Stack
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE
0100
(Beyond the end of the stack)
SP
SP: | 0100
AX: | 1234
BX: | 5678

## Slide 8: How Words Are Added To Stack
00FE
SP:
(Beyond the end of the stack)
SP
AX:
5678
BX:
1234
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE
0100

## Slide 9: How Words Are Added To Stack
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE
0100
(Beyond the end of the stack)
SP
1234
AX:
BX:
5678
00FC
SP:
1234

## Slide 10: POP Instruction
POP instruction removes the last word placed on the stack
SYNTAX: POP destination
  where source is a 16-bit register or memory word
POP instruction causes the contents of SS:SP to be moved to the destination field
It increases the stack pointer (SP) by 2
Restrictions:
      1. PUSH and POP work only with words
      2. Byte and immediate data operands are illegal

## Slide 11: How Words Are Added To Stack
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE
0100
(Beyond the end of the stack)
SP
FFFF
CX:
0001
DX:
00FC
SP:
5678
1234

## Slide 12: How Words Are Added To Stack
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE
0100
(Beyond the end of the stack)
SP
FFFF
CX:
0001
DX:
5678
00FE
SP:
5678
1234

## Slide 13: How Words Are Added To Stack
Offset
0000
00F4
00F6
00F8
00FA
00FC
00FE
0100
(Beyond the end of the stack)
SP
FFFF
CX:
0001
DX:
5678
1234
0100
SP:
5678
1234

## Slide 14: How Words Are Added To Stack
Word 3
Offset
0000
0002
0004
0006
00FA
00FC
00FE
0100
It stack is empty, SP has a value of 100h; otherwise it has a value between 0000-00FEh
SP:
(Beyond the end of the stack)
Word 2
Word 1

## Slide 15: FLAGS Register and Stack
PUSHF
  pushes (copies) the contents of the FLAGS register onto the stack. It has no operands
POPF
  pops (copies) the contents of the top word in the stack to the FLAGS register. It has no operands
NOTES:
  PUSH, POP, and PUSHF do not affect the flags !!
  POPF could theoretically change all the flags because it resets the FLAGS REGISTER to some original value that you have previously saved with the PUSHF instruction

## Slide 16: Example: Fill up the trace table given below.

## Slide 17: Example:
AX = 3245H
BX = 1234H
CX = ABCDH
SP = FEH
PUSH AX PUSH CX POP BX AX =?
BX =? CX =? SP =?
AX = 3245H
BX = 1234H
CX = ABCDH
SP = FEH PUSH BX PUSH CX POP BX POP AX PUSH CX PUSH BX POP CX PUSH AX POP BX AX =?
BX =? CX =? SP =?
AX = 3245H
BX = 1234H
CX = ABCDH
SP = FEH PUSH BX PUSHF POPF PUSH CX POP BX POP AX PUSH CX PUSH BX POP CX PUSH AX POP BX AX =?
BX =? CX =? SP =?

## Slide 18: Important Notes
Not only can the programmer use the stack but DOS can and also does use the stack
In fact DOS uses the stack every time the user executes an
    INT 21h function
Because of the "last-in first-out" nature of the stack, the order that items are removed from the stack is the reverse of the order in which they are placed on the stack

## Slide 19: Example Program
The following code allows a user to input a string consisting of 10 characters and then displays the 10 characters in reverse order on the screen
TITLE DISPLAY THE 10 CHARACTERS TYPED IN REVERSE ORDER
.MODEL SMALL
.STACK 100H
.DATA
CR EQU 0DH
LF EQU 0AH
MESSAGE DB CR,LF,'PLEASE TYPE ANY 10 '
DB ' CHARACTERS',CR,LF,'$'
REVERSE DB CR,LF,'THE CHARACTERS IN REVERSE'
DB ' ARE:',CR,LF,'$'
Note:
0dh is quivalent to 13 in decimal and to carriage return ('\r') in ASCII which moves the cursor to the beginning of the current row.
0ah is equivalent to 10 in decimal and to linefeed ('\n') in ASCII which moves the cursor to the next row of the screen but maintaining the same column.
EQU (Equates) it is used for declaring variables having constants values.

## Slide 20: Example Program (cont’d)
.CODE
MAIN PROC
; ----------------------------INITIALIZE DATA SEGMENT REGISTER
MOV AX,@DATA
MOV DS,AX
;-------------------- SOUND BELL AND PRINT A MESSAGE FOR INPUT
MOV AH,2 ; prepare to display single character
MOV DL,07H ;character is 07H
INT 21H ; display it
MOV AH,9 ; prepare to Displays a message terminated by ‘$’. LEA DX,MESSAGE ; Loads effective address of MESSAGE in DX reg
INT 21H
;-----------------------------ACCEPT CHARACTERS
MOV CX,10
MOV AH,1

## Slide 21: Example (cont’d)
READ:
INT 21H
PUSH AX ;CAN'T PUSH AL SO PUSH AX!
LOOP READ
;-----------------------------PRINT REVERSE MESSAGE
MOV AH,9
LEA DX,REVERSE
INT 21H
;-----------------------------PREPARE TO PRINT IN REVERSE
MOV CX,10
MOV AH,2

## Slide 22: Example (cont’d)
DISP:
POP DX
INT 21H
LOOP DISP
;-----------------------------RETURN TO DOS
MOV DL,CR
INT 21h
MOV DL,LF
INT 21h
MOV AH,4CH
INT 21H
MAIN ENDP
END MAIN

## Slide 23: Terminology of Procedures
Top-down program design
  Decompose the original problem into a series of subproblems that are easier to solve than the original problem
Subproblems in assembler language can be structured as a collection of procedures
Main procedure contains the entry point to the program and can call one of the other procedures using a CALL statement
It is possible for a called sub-procedure to call other procedures
In AL, it is also possible for a called sub-procedure to call itself (recursion)!

## Slide 24: Terminology of Procedures (cont’d)
When the instructions in a called procedure have been executed, the called procedure usually returns control to the calling procedure at the next sequential instruction after the CALL statement
Programmers must devise a way to communicate between procedures - there are no parameter lists !!! Typically in assembler language, procedures often pass data to each other through registers

## Slide 25: Procedures (cont’d)
Procedures should be well-documented
  Describe what the procedure does
  Indicate how it receives its input from the calling program
  Indicate how it delivers the results to the calling program
  Indicate the names of any other procedures that this procedure calls
A procedure usually begins by PUSHing (saving) the current contents of all of the registers on the stack.
A procedure usually ends by POPing the stack contents back into the registers before returning to the CALLing procedure
When writing a procedure, do NOT PUSH or POP any registers in which you intend to return output!!

## Slide 26: Procedure Declaration
name PROC type
; body of procedure RET
name ENDP
User defined name
Optional operand
Near
Statement calls the procedure in the same segment
Far
Statement calls the procedure in the different segment
Causes the control to transfer back to the calling procedure
Every procedure should have a RET coded somewhere within the procedure - usually the last instruction in a procedure

## Slide 27: PROC Instruction
PROC instruction establishes a procedure
Procedure declaration syntax:
    name PROC
    ; body of the procedure
      RET
    name ENDP
name is a user-defined variable.
RET instruction causes control to transfer back to the calling Procedure.
Every procedure should have a RET coded somewhere within the procedure - usually the last instruction in a procedure
Main PROC
CALL PROC1
next instruction
PROC1 PROC
next instruction
RET

## Slide 28: Before Call
0010 | Main PROC CALL PROC1
0012 0020 | next instruction PROC1 PROC next instruction RET
00FC
00FE
0100

## Slide 29
COMMUNICATION BETWEEN PROCEDURES
Programmers must devise a way to communicate between procedures –
there are no parameter lists !!!
Typically in assembler language, procedures often pass data to each other through registers

## Slide 30: Procedures Documentation
Procedures should be well-documented
  Describe what the procedure does
  Indicate how it receives its input from the calling program
  Indicate how it delivers the results to the calling program
  Indicate the names of any other procedures that this procedure calls
; Describe what the procedure does
; | input: | Indicate how it receives its input from the calling program
; | output: | Indicate how it delivers the results to the calling program
; | uses: | Indicate the names of any other procedures that this procedure calls

## Slide 31: Procedures (cont’d)
A procedure usually begins by PUSHing (saving) the current contents of all of the registers on the stack.
A procedure usually ends by POPing the stack contents back into the registers before returning to the CALLing procedure
When writing a procedure, do NOT PUSH or POP any registers in which you intend to return output!!

## Slide 32: CALL Instruction
A CALL instruction invokes a procedure
SYNTAX: CALL name (direct CALL)
    where name is the name of a procedure.
Executing a CALL instruction causes the following to happen:
  The return address of the CALLing program which is in the IP register is pushed (saved) on the STACK. This saved address is the offset of the next sequential instruction after the CALL statement (CS:IP)
  The IP then gets the offset address of the first instruction in the procedure

## Slide 33: RET Instruction
RET statement cause the stack to be popped into IP. Procedures typically end with a RET statement.
Syntax: RET
Once the RET is executed, CS:IP now contains the segment offset of the return address and control returns to the calling program
In order for the return address to be accessible, each procedure must ensure that the return address is at the top of the stack when the RET instruction is executed.

## Slide 34: Before Call
0010 | Main PROC CALL PROC1
0012 0020 | next instruction PROC1 PROC next instruction RET
00FC
00FE
0100

## Slide 35: AFTER Call
Main PROC
CALL PROC1
next instruction
0010
0012
PROC1 PROC
next instruction
RET
0020
00FE
0100
00FC

## Slide 36: Before RET
Main PROC
CALL PROC1
next instruction
0010
0012
PROC1 PROC
next instruction
RET
0020
00FE
0100
00FC
0030

## Slide 37: After RET
Main PROC
CALL PROC1
next instruction
0010
0012
PROC1 PROC
next instruction
RET
0020
00FE
0100
00FC
0030

## Slide 38: Typical Layout of a Program Containing Procedures
TITLE A PROGRAM THAT CONTAINS SEVERAL PROCEDURES
.MODEL SMALL
.STACK 100H
.DATA
;*** define data elements here *******
.CODE
MAIN PROC
; INITIALIZE DATA SEGMENT REGISTER
MOV AX,@DATA
MOV DS,AX
;*** code any necessary statements here ***
;*** get ready to call procedure ABC by ***
;*** first moving input values to appropriate registers ***
CALL ABC

## Slide 39: Typical Layout (cont’d)
;*** code any necessary statements here ***
;*** get ready to call procedure DEF by ***
;*** first moving input values to appropriate registers ***
CALL DEF
;*** code any necessary statements here ***
;*** get ready to call procedure GHI by ***
;*** first moving input values to appropriate registers ***
CALL GHI
;*** code any necessary statements here ***
; RETURN TO DOS
MOV AH,4CH
INT 21H
MAIN ENDP

## Slide 40: Typical Layout (cont’d)
ABC PROC
PUSH ..... ; as many PUSHes as you need
POP ..... ; POPs in reverse order of PUSHes
RET
ABC ENDP
;
DEF PROC
PUSH ..... ; as many PUSHes as you need
POP ..... ; POPs in reverse order of PUSHes
RET
DEF ENDP
;

## Slide 41: Typical Layout (cont’d)
GHI PROC
PUSH ..... ; as many PUSHes as you need
POP ..... ; POPs in reverse order of PUSHes
RET
GHI ENDP
END MAIN

## Slide 42: Example Program
Now let’s study the Multiplication Procedure
Product = 0
Repeat
IF lsb of B is 1
then
= product + A
product end_if shift left A
shift right B
Until B = 0

## Slide 43: Example Program (cont’d)
TITLE MULTIPLICATION BY ADDING AND SHIFTING (8 BITS BY 8 BITS)
.MODEL SMALL
.STACK 100H
.CODE
MAIN PROC
;------------------------------> INITIALIZE AX AND BX
MOV AX,13 ;SOME ARBITRARY VALUE
MOV BX,10 ;SOME ARBITRARY VALUE
;------------------------------> INVOKE PROCEDURE
CALL MULTIPLY
;------------------------------> DX NOW CONTAINS PRODUCT
; RETURN TO DOS
MOV AH,4CH
INT 21H
MAIN ENDP

## Slide 44: Example (cont’d)
MULTIPLY PROC
;-----------------------------> THIS PROCEDURE MULTIPLIES THE
;-----------------------------> VALUE IN AX BY THE VALUE IN BX
;-----------------------------> RETURNING THE PRODUCT IN DX.
;-----------------------------> VALUES IN AX AND BX ARE LIMITED ;-----------------------------> TO 00 - FFh.
;-----------------------------> IT USES SHIFTING AND ADDITION
;-----------------------------> TO ACCOMPLISH THE MULTIPLICATION
PUSH AX ; DON'T DESTROY AX
PUSH BX ; DON'T DESTROY BX
XOR DX,DX ; CLEAR DX WHERE PRODUCT WILL BE
REPEAT:
TEST BX,1 ; IS LSB = 0?
JZ END_IF
ADD DX,AX ; PRODUCT = PRODUCT + A
END_IF:
SHL AX,1
SHR BX,1
JNZ REPEAT
POP BX
POP AX
RET
MULTIPLY ENDP
END MAIN

## Slide 45: Important Notes on Stack
PUSHES AND POPS are often used to save data temporarily on the program stack. They are also used implicitly each time a CALL and a RETurn sequence is executed.
Remember that the SP is decremented BEFORE placing a word on the stack at PUSH time but it is incremented AFTER removing a word from the stack at POP time.
If, for some reason, you want a copy of the FLAGS register in BX, you can accomplish this by:
PUSHF
POP BX
Stack allows you to save the contents of a register, use the register for something else temporarily, and the restore the register to its original value.

## Slide 46: Notes on Stack (cont’d)
Pushing and popping the contents of registers is preferable to storing their contents as variables in the DATA segment
Reasons:
  Using the stack is more economical. Instead of allocating data space, by pushing and popping data into the stack, you use space as you need it and release it when you no longer need it.
  Since the 8088/8086 allows recursion, if a routine called itself and saved the contents of a register to a data location each time it was invoked, it would be overwriting the previous contents of that location with each recursion!
  Using a stack instead of a data location makes code more portable. Once you have written a good routine, you may choose to incorporate that routine into several different programs. Or if you are working with a programming team piecing smaller subroutines into a one larger main routine, subroutines that do their work without referencing particular data locations are more easily patched into main programs than subroutines that do reference particular data locations. Therefore, should not refer to ANY variable data names in ANY procedure that you write!!!'

## Slide 47: Notes on Stack (cont’d)
Care must be taken not to corrupt the STACK because not only does it save values for the programmer but it also saves values for the CPU. These values get interwoven on the stack. If the SP becomes confused, the CPU could get lost throwing your computer into a system error!!
Always check to see that the PUSHES and POPS in a program are paired --- or --- at least that each of them is balanced by program code that restores the stack pointer to its proper value.
If you find yourself in the middle of a system error, more than likely you look for a problem in the way you implemented the stack.

## Slide 48: Example Procedure on Safe Use of Stack
A procedure to display a carriage return and a line feed:
CRLF PROC
PUSH AX ; Save AX
PUSH DX ; Save DX
MOV AH,2 ; Display a Carriage Return
MOV DL,0Dh
INT 21h
MOV DL,0Ah ; Display a Line Feed
INT 21h
POP DX ; Restore DX
POP AX ; Restore AX
RET
CRLF ENDP

## Slide 49: Example (cont’d)
This procedure can be called by the programmer at any time regardless of what is in his/her AX or DX registers. As far as the programmer is concerned, all you know is that this procedure issues the CR/LF sequence to the console and all of your registers will be unchanged when the procedure has finished executing!

## Slide 50: Example: A program that inputs 10 numbers and prints their sum
TITLE printsum
.data ;data segment
MSG1 DB 'Please enter a number', 10, 13, '$'
MSG2 DB 'sum = ', 10, 13, '$'
SUM DB 0
.stack 100h
.code ;code segment
MAIN PROC
start: mov ax,@data
mov ds,ax
MOV CX, 10 ;10 repetitions
REPEAT: CALL INPUT ;call to input proc
CALL SUMMATION ;call to sum proc
LOOP REPEAT
MOV AL, SUM
MOV BL, 10
MOV AH,0
DIV BL ;dividing with 10
PUSH AX ;saving division result to stack
LEA DX,MSG2
MOV AH, 09 ;printing MSG2
INT 21H
POP DX ;printing digit 1
PUSH DX
ADD DL, 30H
MOV AH, 02
INT 21H
POP DX
MOV DL, DH ;printing digit 2
ADD DL, 30H
MOV AH, 02
INT 21H

## Slide 51: Example (continued)
MOV AH,4CH ; exit to operating system
INT 21H
MAIN ENDP
INPUT PROC NEAR ;INPUT PROCESS
LEA DX,MSG1 ;OR MOV DX, OFFSET MSG1
MOV AH,09H ; Printing MSG1
INT 21H
MOV AH,01H
INT 21H ;reading number 1 from keyboard
SUB AL, 30H ;careful, no check for valid number!
RET
INPUT ENDP
SUMMATION PROC NEAR ;SUM PROCESS
ADD SUM, AL ;Adding the two numbers
RET
SUMMATION ENDP
end start

## Slide 52: Example 2 (1/3): A program that inputs 10 numbers and prints their maximum
TITLE findmax
.data ;data segment
MSG1 DB 'Please enter a number', 10, 13, '$'
MSG2 DB ‘max = ', 10, 13, '$'
MAX DB 0
.stack 100h
.code ;code segment
MAIN PROC
start: mov ax,@data
mov ds,ax
MOV CX, 10 ;10 repetitions
REPEAT: CALL INPUT ;call to input proc
CALL maxfind ;call to sum proc
LOOP REPEAT
CALL maxprint
MOV AH,4CH ; exit to operating system
INT 21H
MAIN ENDP

## Slide 53: Example 2 (2/3)
INPUT PROC NEAR ;INPUT PROCESS
LEA DX,MSG1 ;OR MOV DX, OFFSET MSG1
MOV AH,09H ; Printing MSG1
INT 21H
MOV AH,01H
INT 21H ;reading number 1 from keyboard
SUB AL, 30H ;careful, no check for valid number!
RET
INPUT ENDP
MAXFIND PROC NEAR ;SUM PROCESS
CMP MAX, AL ;Adding the two numbers
JAE SKIP
MOV MAX, AL
SKIP: RET
MAXFIND ENDP

## Slide 54: Example 2 (3/3)
MAXPRINT PROC NEAR
LEA DX,MSG2
MOV AH, 09 ;printing MSG2
INT 21H
MOV DL, MAX ;printing MAX
ADD DL, 30H
MOV AH, 02
INT 21H
RET
MAXPRINT ENDP
END START

## Slide 55: Example 3: Counting capital letters in a string starting in memory string and ending with the # character
TITLE findmax
.data ;data segment
STRING DB ‘wgE@%^@45gAJde#ERty’
MSG2 DB ‘No of CAPS = ', 10, 13, '$'
CAPS DB 0
.stack 100h
.code ;code segment
MAIN PROC
start: mov ax,@data
mov ds,ax
REPEAT: CALL CAPSCOUNT ;call to proc
CALL print
MOV AH,4CH ; exit to operating system
INT 21H
MAIN ENDP

## Slide 56: Example 3 (2/3)
CAPSCOUNT PROC NEAR
MOV SI,0
REPEAT: CMP STRING[SI], ‘#’
JE SKIP ;end of string
CMP STRING[SI], ‘A’
JB NOTCAPS
CMP STRING[SI], ‘Z’
JA NOTCAPS
INC CAPS ;no jump, so capital letter
NOTCAPS: INC SI ;increment pointer to check next
JMP REPEAT
SKIP: RET
CAPSCOUNT ENDP

## Slide 57: Example 4:
Write a program that reads a 4-number PIN ending with ‘enter’ and accepts it or rejects it. The user has three attempts to enter the valid PIN which is 4519. The PIN numbers should not be displayed and instead ‘X’ should be printed.
.data
MSG1 db 'Please enter PIN and press enter', 10, 13, '$'
MSG2 db 'PIN accepted', 10, 13, '$'
MSG3 db 'Incorrect PIN, please try again', 10, 13, '$'
MSG4 db 'PIN error', 10, 13, '$'
repeat db 0
PIN db '4519'
user db 4 dup(?) ;user input
Failed db 0 ;number of failed input
.stack 100h

## Slide 58: Example 4 (continued)
.code
Main proc near
Start: mov ax,@data
mov ds,ax
Again: call input
call pincheck
call output
cmp repeat, 1
je again
mov ah, 4ch ;end of program
int 21h
Main endp

## Slide 59: Example 4 (continued)
Input proc near
lea dx, msg1 ;printing prompt msg
mov ah, 09h
int 21h
mov si, 0 ;pin counter
read: mov ah, 01h ;reading pin number
int 21h ;without displaying it
cmp AL, 13 ;checking for enter
je skip
mov user[si], al ;saving input on memory
inc si ;incrementing counter
mov dl,'X' ;displaying ‘X’
mov ah,02h
int 21h
jmp read
skip: ret
Input endp

## Slide 60: Example 4
Pincheck proc near
mov cx, si ;counter
Check: mov al, user[si-1]
cmp PIN[si-1], al
jne error
dec si
loop check
lea dx, msg2 ;correct PIN
mov repeat,0
jmp skip2
Error: inc failed
cmp failed, 3
je failure
lea dx, msg3
mov repeat,0
jmp skip2
Failure: lea dx, msg4
mov repeat,1
Skip2: ret
Pincheck endp

## Slide 61: Example 4 (continued)
Output proc near
mov ah, 09h ;printing message
int 21h
ret
Output endp
End start

## Slide 62: EXAMPLE 5 (encode a text sequence using the trithemius cipher)
The trithemius cipher replaces the first letter of a message with the next letter in the alphabet (A becomes B), the second letter of a message with the letter two places after it (A becomes C), the third with the letter three places after it (A becomes D)
Example: NICEDAY becomes OKFIIGF
The text ends with the $ character and does not contain spaces

## Slide 63
.data
Unencoded db ‘NICEDAY$’
Encoded db ?
.stack 100h
.code
MOV AX, @data
MOV DS, AX
CALL ENCODE ;message encoding procedure
CALL PRINT ;printing procedure
MOV AH,4CH
INT 21H

## Slide 64
ENCODE PROC NEAR
MOV SI,0 ;pointer for message
REPEAT: MOV AL, unencoded[SI]
CMP AL, '$'
JE SKIP ;end of message
MOV AH,0
ADD AX, SI ;adding 1 for 1st character
INC AL ;2 for 2nd , 3 for 3rd etc.
CMP AL, 'Z'
JB SKIP2 ;no wraparound
SUB AL, 26 ;number of letters in latin alphabet
SKIP2: MOV encoded[SI], AL
INC SI
JMP REPEAT
SKIP: RET
ENCODE ENDP

## Slide 65
PRINT PROC NEAR
MOV CX, SI
MOV SI,0
PRINTLOOP: MOV DL, encoded[SI]
MOV AH, 02H
INT 21H
INC SI
LOOP PRINTLOOP
RET
PRINT ENDP

## Slide 66: Example 6
Write a program that bubble sorts an array of 20 1-byte numbers in memory location ARRAY in ascending order.
do
swapped := false
for (i=0; i < 20 ; i++)
if A[ i ] > A[ i + 1 ] then
swap( A[ i ], A[ i + 1 ] )
swapped := true
end if
end for
while swapped

## Slide 67
.data
ARRAY DB 02H, 03H, 43H, 41H, 92H, ADH, 33H, F2H, 92H, 47H, 84H, 56H, 66H, 62H, AAH, 12H, C2H, 28H, 99H, 33H
SWAP db 0 ;boolean
.stack 100h
.code
MOV ax, @data
MOV ds, ax
REPEAT: MOV SWAP, 0 ;swap = false
MOV CX, 20 ;counter
MOV SI, 0 ;pointer
AGAIN: MOV AL, ARRAY[SI] ;comparing adjacent numbers using AL
CMP AL, ARRAY[SI+1] ;cannot compare directly
JBE SKIP
MOV BL, ARRAY[SI+1] ;temp ;switching through BL and AL
MOV ARRAY[SI], BL
MOV ARRAY[SI+1], AL
MOV SWAP, 1 ;swap = true
SKIP: INC SI
LOOP AGAIN
CMP SWAP, 1 ;if swap = true, not sorted, run again
JE REPEAT ;else finished
MOV AH, 4CH ;program ends
INT 21H

## Slide 68: Example 7
Write an assembly program that counts the occurrences of the string “CAT” in a larger string ending with ‘$’
.data
STRING DB ‘adrEADTYCATDR3448Grtcatdfe$’
MATCH DB ‘CAT’
COUNT DB 0 ;NUMBER OF OCCURRENCES
.stack 100h

## Slide 69
.code
START: MOV ax, @data
MOV ds, ax
MOV COUNT, 0 ;number of occurrences originally zero
MOV SI,0 ;pointer
REPEAT: MOV AL,STRING[SI] ;loop body
CMP AL, '$‘ ;checking for ‘$’ first
JE FINISH ;if ‘$’, end of string
INC SI ;otherwise increment pointer
CMP AL,MATCH[0] ;looking for first character
JNE SKIP ;not first character, check next
NEXT: MOV AL, STRING[SI] ;otherwise fetch next character
CMP AL, MATCH[1] ;and compare with the second one
JNE SKIP ;second character no match
NEXT2: INC SI ;second character match
MOV AL, STRING[SI] ;fetch next character and
CMP AL, MATCH[2] ;compare with last
JNE SKIP ;no match, fetch next
INC COUNT ;match found, increment counter
SKIP: JMP REPEAT ;repeat until ‘$’ is found
FINISH: MOV DL, COUNT ;printing counter
ADD DL, '0‘ ;moving to DL to print
MOV AH, 02H ;printing character interrupt
INT 21H
MOV AH, 4CH ;end of program
INT 21H
END START

## Slide 70: Example 8
Write an assembly program that counts the occurrences of the stringS “CAT”, “cat”, “cAt”, “CAt:” etc. (case insensitive) in a larger string ending with ‘$’
.data
STRING DB ‘adrEADTYCATDR3448Grtcatdfe$’
MATCH1 DB ‘CAT’
MATCH2 DB ‘cat’
COUNT DB 0 ;NUMBER OF OCCURRENCES
.stack 100h

## Slide 71
.code
START: MOV ax, @data
MOV ds, ax
MOV COUNT, 0
MOV SI,0
REPEAT: MOV AL,STRING[SI]
CMP AL, '$'
JE FINISH
INC SI
CMP AL,MATCH1[0]
JNE TRY1
JMP NEXT
TRY1: CMP AL, MATCH2[0]
JNE SKIP
NEXT: MOV AL, STRING[SI]
CMP AL, MATCH1[1]
JNE TRY2
JMP NEXT2
TRY2: CMP AL, MATCH2[1]
JNE SKIP
NEXT2: INC SI
MOV AL, STRING[SI]
CMP AL, MATCH1[2]
JNE TRY3
INC COUNT
JMP SKIP
TRY3: CMP AL, MATCH2[2]
JNE SKIP
INC COUNT
SKIP: JMP REPEAT
FINISH: MOV DL, COUNT
ADD DL, '0'
MOV AH, 02H
INT 21H
MOV AH, 4CH
INT 21H
END START